## Slide 1: Friendly introduction to Robotic Estimations
Dor Israeli
Robotic Motion Planning course, 2019
Some sketches from the great Kalman and Bayesian Filters in Python by Roger R. Labbe

## Slide 2: OR Realistic Motion Planning

## Slide 3: Lacking initial knowledge
Image by
http://lazygamer.co/

## Slide 4: Systems are usually dynamic
Image by
geoawesomeness.com/

## Slide 5: Imperfect execution
Image by
www.indiamart.com/

## Slide 6: Estimations in Robotic Motion Planning
Understand environment(obstacles, radiation, temp., …)
Understand self (position, velocity, battery, …)
Stop if done
Solve robotic plan (constraints, optimization, …)
Execute next step
Goto 1

## Slide 7: Agenda
1
Tracking a Dynamical system
2
Naive approaches
3
The Kalman Filter
4
Nonlinear Filters

## Slide 8: Tracking a Dynamical system

## Slide 9: What is a Static System?
Noisy measurements are given offline
Measurements describe the same situation (different readers, POVs, ...)
Usually solved using least mean squares
For example:
  Measuring your height, by measuring several times and averaging
  Calculating linear trend of points on a graph
  Trying to locate yourself using triangulation (by a river, 1 km near the building)

## Slide 10: What is a Dynamical System?
Noisy measurements are given online
The state evolves with time (e.g. physical motion)
There is a connection (known or not) between states
Our understanding may change according to new findings
Goal is usually to accurately track some changing quality and predict its future state
For example:
  A/C tracking and affecting room temperature
  Autonomous car navigating using GPS+Accelerometer
  Tracking a bird using reverse-GPS

## Slide 11: So, why is it hard?
No theory
Inaccurate theory
Complex theory
Noisy measurements
Real-time
Spontaneous disturbances
...

## Slide 12: Simple example: Quadcopter with constant power
A quadcopter was at some known previous height and it’s engine is at constant output:
Our noisy instrument measures the copter’s height every fixed interval
We’d like to track and predict the copter’s height as accurately as possible in real-time

## Slide 14: Can’t I just use the measurements?
Pros:
  Doesn’t require dynamics theory
  Doesn’t require resources (time, cpu, etc)
  Doesn’t diverge
  Standard deviation is known
Cons:
  Does not leverages known theory
  Instrument’s standard deviation might be too big
  Results are usually not smooth
  Results are sometimes not sensible
  Sometimes the instruments misses a measure
  ...

## Slide 15: Naive approaches

## Slide 16: Moving Average Algorithm
As a prediction, output the weighted mean of the last N measurements
Assumptions:
  Measurements in close range describe the similar states
  If given several measurements of the same state, it’s safest to assume the (weighted) mean
Pros:
  Applicable when no specific dynamic is known
  Gets better upon increasing resolution
Cons:
  Can’t use known theory
  Usually lags
  Will err and not converge if the function changes too quickly
  Can’t combine with different types of measurements or knowledge

## Slide 17: Bad robotic use case- fast changing world
Image by
auto.howstuffworks.com/

## Slide 18: Online Least Mean Squares Algorithm
Each time step, look at the problem as a static system
Trying to fit given measurements into some assumed linear theory, e.g:

## Slide 19: Online Least Mean Squares continued
Pros:
  Makes use of some theory
  outputs sensible results and latent variables
Cons:
  requires a linear theory to fit into
  Usually can’t use previous calculations
  Might diverge on noisy measurements or inexact theory
  Might be inexact and expensive in nonlinear cases

## Slide 20: Bad robotic use case- time critical situations
Image by
dronerush.com/

## Slide 21: 𝛂-𝛃 Filters
Many systems can be approximated to have a constant rate of change
  Higher dimensions variations exist, but usually irrelevant because interactions are too complex
  Lower dimension is the moving average algorithm!
Predict: extrapolate our previous calculated state using calculated rate of change
Update: Find weighted mean with current given measurement (using the 𝛂-𝛃 ratios)

## Slide 22: 𝛂-𝛃 Filters continued
Pros:
  Makes more balanced use of both theory and measurements
  Handles noise or inaccurate theory better
  Doesn’t require resolving entire system
  May combine different types of measurements
Cons:
  Ratios are set manually by trial and error
  Requires some theory
  Might not converge to correct result
  Hard-coded ratios handles changing dynamics poorly
  Effectively supports just two dimensions (position, velocity)

## Slide 23: Bad robotic use case- Changing Environment
Image by
www.forbes.com/

## Slide 24: The Kalman Filter

## Slide 25: Kalman Filter as a Bayesian 𝛂-𝛃 Filter
The 𝛂-𝛃 Filter is a good start, but dynamic 𝛂-𝛃 ratios are a better idea:
  Spares us the research needed for each new system configuration
  Finds more accurate ratios
  Ratios could change over evolution
Represent our belief as a probability gaussian:
  thesis as mean and confidence as variance
  The more confident a belief is, the more influential photos provided by Greuel, Gert-Martin
Can converge to the ideal 𝛂-𝛃 Filter

## Slide 26: Intuition in 1D: prediction step
Prior state xi-1~N(μx|i-1, σx|i-1²)
After a time interval (𝚫t) at some speed with some confidence, vi-1~N(μv|i-1, σv|i-1²)

## Slide 27: Moving with uncertainty

## Slide 28: Algorithm steps: predict & update

## Slide 29: Intuition in 1D: update step
Upon receiving new measurement m~N(μm, σm²)

## Slide 30: Kalman Gain
We define the Kalman Gain as Ki=σprior|i²/(σprior|i²+σm|i²), and ri=μm|i-μprior|i
  μposterior|i = μprior|i+Ki⋅ri
  σposterior|i²= σprior|i⋅(1-Ki)
Ki is the dynamically calculated 𝛂 ratio!

## Slide 31: Formalization: Univariate Kalman Filter
Looking at the 1D problem (Gaussians) gave us intuition, but the true power lies in higher dimensions
In order to support higher dimensions we first need to formalize in scalar Kalman form:

## Slide 32: Formalization: Multivariate Kalman Filter
We want to support more variables
  Multiple observed states (e.g: x sensor and vy sensor)
  Multiple unobserved states (e.g: clock offset)
  Maybe some are in our control
  Cross correlation

## Slide 33: Practical Example

## Slide 34: Bad robotic use case- nonlinear model
Image by
https://imgur.com/user/gabiekur

## Slide 35: Nonlinear Filters

## Slide 36: The problem with nonlinearity
For example, one distance sensor says 50km and one angle sensor says 90 degrees
We can’t use Kalman filter as is
  Because nonlinearity ruins our prediction gaussianity

## Slide 37: Quadcopter with nonlinear air resistance
Resistance is proportional to velocity squared and against it:

## Slide 38: Unscented Kalman Filter

## Slide 39: More nonlinear algorithms
The Extended Kalman filter
  Approximate 1st order using Jacobian matrix
The Particles Filter
  Simulate thesys using a lot of weighted particles
  Very Robust, Very demanding
And many more variations!
  My Thesis will also be one :)

## Slide 40: Thank you ☺