## Slide 1: Computer haptics

## Slide 2: Introduction

## Slide 3
hearing
sight
smell
taste
touch
which sense is most valuable to you?
which would you relinquish last?
Notes: - Interesting cultural differences: I once gave a talk to a group of engineers and executives from Hyundai (all Korean). The majority decision there was smell! Also, maybe their highest-ranking officer (a VP) influenced them.
- My goal is not to convince you that touch is the *most* important. Just that it *is* important, as are all the senses. By thinking about our sensory experiences, we can open up new ways of thinking about the world and our interactions with it.
- What does the sense of touch encompass? Skin + Muscles/joints. Skin is the largest organ in the body!

## Slide 4
hap·tic ('hap-tik)
adj. Of or relating to the sense of touch. [Greek haptikos, from haptesthai, to grasp, touch. (1890)]
Temperature
Texture
Slip
Vibration
Force
Location/configuration
Motion
Force
Compliance
Cutaneous
Kinesthesia
The haptic senses work together with the motor control system to:
Coordinate movement
Enable perception
Johansson and Westling
Notes: There are two components to haptic sensation: Kinesthetics and Cutaneous components
Kinesthetic: refers to force / proprioception. It allows us to sense large scale forces, and know where our limbs our in space or where they are with respect to our own body or another object.
Cutaneous: the cutaneous information specifically refers to anything information you can gather from your fingertips.

## Slide 5: Missing tactile sense
https://www.youtube.com/watch?v=0LfJ3M3Kn80

## Slide 6: Missing kinesthesia
Ian Waterman suffers from sensory neuropathy
Notes: http://www.youtube.com/watch?v=FKxyJfE831Q
This clip is from the 1998 BBC documentary entitled "The Man Who Lost His Body." The film follows Ian Waterman, who at 19 caught a virus that destroyed half of his nervous system, and robbed him of his proprioception. As a result, Ian is unable to mentally sense the relative positions of his limbs in space and whether or not they are in motion. The medical establishment believed that he would never walk again, but through sheer will-power Ian has been able to develop new neural pathways that enable him to function relatively normally. http://en.wikipedia.org/wiki/Proprioception The majority of movements and processes in a healthy adult are carried out unconsciously. However, because of Ian's disorder, he must deliberately focus all of his efforts on even the simplest of tasks (such as sitting up or displaying hand gestures). The full BBC documentary can be found here: Part 1: http://www.veoh.com/browse/videos/category/educational/watch/v15575943NZBjG7Fa Part 2: http://www.veoh.com/browse/videos/category/educational/watch/v15575944ra4F58Ha

## Slide 7: Stereognosis
The mental perception of depth or three-dimensionality by the senses, usually in reference to the ability to perceive the form of solid objects by touch.
Klatzky et al., 1985 – 100 objects are identified within 2 sec
Astereognosis – neurological disorder
  Following stroke and other

## Slide 8
sight
centralized
broad
passive
cognitive
touch
distributed
narrow
active
physical

## Slide 9: Missing haptics – robot-assisted surgery

## Slide 10: Visual substitution does not necessarily help
error (deg)
Yamamoto et al., 2009

## Slide 11: Missing haptics - teleoperation

## Slide 12: Missing haptics - prosthetics

## Slide 13: Missing haptics - BCI
https://youtu.be/AB5vYz1-T_Y

## Slide 15: Haptic applications
Entertainment
Nintendo
Human-Computer Interfaces
BMW
Samsung

## Slide 16: Teleoperation

## Slide 17: Rehabilitation and prosthetics

## Slide 18: Computer-aided design
Boeing Phantom Works

## Slide 19: Education
Immersion

## Slide 20: Computer haptics
The goal of haptic rendering is to enable a user to touch, feel, and manipulate virtual/remote objects through a haptic interface
  Simple static geometry
  Surface texture
  Deformable shapes
  Dynamic behavior

## Slide 21: Haptic loop – virtual reality
user
haptic
device
Virtual
environment rendering algorithm
Sensing of user input:
motion, force, EMG
Actuation to convey touch information:
kinesthetic, tactile

## Slide 22: Haptic loop – teleoperation
user
haptic
device
Teleoperated
environment sensing
Sensing of user input:
motion, force, EMG
Actuation to convey touch information:
kinesthetic, tactile

## Slide 23: Multidisciplinary haptics
Robotics and telerobotics
Computational geometry and computer graphics
Psychophisics, cognitive sciences, and neuroscience
Design
Algorithms
Requirements

## Slide 24: Virtual reality application structure
30Hz
1KHz
Visual: screen, head mounted display
Audio: speakers, headphones

## Slide 25: Haptic device design

## Slide 26: Haptic device
Exchanges energy with the user

## Slide 27: Haptic device classification
Grounding location
  Interdigital devices, body-based exoskeletons, ground-based force reflecting joysticks, and desktop devices
Mechanical behavior
  Impedance: read position, send force
    Cheap, simple design
      Sensable phantom
  Admittance: read force, send velocity/position
    High forces
      Haptic Master

## Slide 28: Haptic device classification
Number of DOF’s
  Motion
    Sensed or not sensed
  Force
    Actuated or not actuated
Sensable Phantom Desktop
  6 sensed motion DOF’s and 3 actuated DOF’s

## Slide 29: Haptic device classification

## Slide 30: Good haptic device
Inertia and friction – low
Back-drivable
Kinematics - minimal constraints on motion
Symmetric inertia, friction, stiffness, and resonate frequency properties
Balanced range, resolution, and bandwidth of position sensing and force reﬂection
Proper ergonomics
  Pain, or even discomfort, can distract the user, reducing overall performance.

## Slide 31: Quantifying haptic device performance
Manipulability – product of singular values of Jacobian
Mechanism isotropy – the ration between the largest and the smallest singular values of the Jacobian
Minimum force output – the maximum of force output in the worst direction

## Slide 32: Sensors
Encoders
Joint position, velocity
Resolution affects also maximum stable stiffness
Magnetic sensors
Force sensors
Strain gouge, load cell
Calibration, drift, thermal sensitivity

## Slide 33: Actuators and transmission
Low inertia, low friction, low torque ripple, back-driveability, low backlash
Use a good motor!
Capstan drive
Friction drive

## Slide 34: Haptic paddle example
500 counts per turn, quadrature leads to 2000 counts per turn, 2.24x10-5m resolution
Desired current
Current amplifier
Current to motor
Torque from motor
Force through capstan
Torque on handle

## Slide 35: Haptic rendering

## Slide 36: Rendering cycle
Sensing
Kinematics
Collision detection
Determining surface point
Force calculation
Statics
Actuation

## Slide 37: System architecture
Avatar: virtual representation of the haptic interface through which the user physically interacts with the virtual environment.
HIP – haptic interaction point

## Slide 38: System architecture
Between HIPs and objects
1KHz
Notes: Low-level control algorithms sample the position sensors at the haptic interface device joints.
These control algorithms combine the information collected from each sensor to obtain the position of the device-body interface in Cartesian space
  The avatar’s position inside the virtual environment.
The collision-detection algorithm uses position information to ﬁnd collisions between objects and avatars
  Report the resulting degree of penetration or indentation.
The force-response algorithm computes interaction forces between avatars and virtual objects
The force-response algorithm sends interaction forces to the control algorithms
  Apply them on the operator through the haptic device while maintaining a stable overall behavior

## Slide 39: Force response algorithms
Rigid objects
Soft, deformable objects
Dynamic objects
Haptic playback
More than one operator

## Slide 40: 1 DOF interaction
Examples:
  Door knob, scisors, pressing syringe piston
Virtual wall

## Slide 41: Staircase effect
Low stiffness – soft wall
High stiffness – unstable interaction

## Slide 42: 3 DOF interaction
Vector fields – one to one mapping between position and force
IHIP, god object, proxy algorithms that take into account the history of interaction

## Slide 43: Surface detailes
Smooth surfaces – force shading
Friction
Texture
  Image based – texture map of heights wrapped around the object
  Noise, fractals

## Slide 44: More than 3 DOF – ray based
The interaction is with a line segment
Models of long tools
  Surgical instruments simulation

## Slide 45: More than 3 DOF - complex probing tool
A set of points on the probing tool is simulated
Appropriate for models of mechanical assembly

## Slide 46: Deformable objects
Geometry based
  Fast, easy to implement
  Don’t simulate the mechanics
    Vertex v. spline
Physics based
  Realistic behavior
  Computationally expensive
    Particle based, Finite elements based
Loose coupling between force and position deformation

## Slide 47: Dynamic objects

## Slide 48: Shared haptic operation
Karniel, Nisky, Avraham, Peles, and Levy-Tzedek, 2010

## Slide 49: Vibration feedback
Render texture
Render contact transients and increase perceived stiffness
Sensory substitution

## Slide 50: Example Verro-touch
Katherine Kuchenbecker

## Slide 51: Wearable Haptics

## Slide 52: Non-grounded Haptics

## Slide 53: Tactile Haptics
https://youtu.be/610iTKlYBVM

## Slide 54: Tactile arrays

## Slide 55: TPAD – ultrasonic friction modulation

## Slide 56
http://hapkit.stanford.edu

## Slide 57: Particle Jamming Haptics

## Slide 58: Particle Jamming Haptics

## Slide 59: The future of haptics
Journal
  IEEE Transactions on Haptics
International conferences
  EuroHaptics 2016
    http://www.eurohaptics.org/
  Haptics Symposium
    http://2016.hapticssymposium.org/
  WorldHaptics 2017
    http://www.worldhaptics2017.org/
Technical committee on haptics
  http://www.worldhaptics.org/
IEEE the Institute, March 2008
Notes: מה שמערכות הניתוח הרובוטי (ולכן גם הניתוח מרחוק) לא מספקות כרגע הוא תחושת המגע.
רופאים רבים מדווחים כי פרוצדורות היו מתבצעות יותר טוב ויותר מהר אם תחושת המגע ומשוב הכוח היו זמינות
מחקרים רבים שנעשו בהפעלה מרחוק דו-צדדית העלו כי הביצועים טוביםן יותר אם הכוח שמוזן הוא אמין, אינפורמטיבי ולא מייצר בעיות של יציבות

## Slide 60: References
Basdogan, C. and M. A. Srinivasan (2002). "Haptic Rendering in Virtual Environments." Handbook of Virtual Environments. K. Stanney. London, Lawrence Earlbaum, Inc.: Chapter 6, pp. 117-134
Biggs, J. and M. A. Srinivasan (2002). "Haptic Interfaces. Handbook of Virtual Environments." K. Stanney. London, Lawrence Earlbaum, Inc.: Chapter 5, pp. 93-116.
Salisbury, Conti, and Barbagli (2004). “Haptic rendering: Introductory concepts” in IEEE Computer Graphics and Applications, pp. 24-32
Massie and Salisbury (1994) “The PHANTOM Haptic Interface: A Device for Probing Virtual Objects” Proceedings of the ASME Winter Annual Meeting, Symposium on Haptic Interfaces for Virtual Environment and Teleoperator Systems, Chicago, IL, Nov. 1994.
Hannaford B., and Okamura A. (2017), “Haptics” in: Handbook of Robotics.